Documentation for ct_boxplot

Feb. 4, 1999

by Darrin Stewart and Michael Zuker

Documentation for ct_boxplot


Files

ct_boxplot_setcolor.inc  Sets the colors
ct_boxplot.col           List of colors to use 
copyright_ps.inc         Displays the copyright message  the ps output
copyright_img.inc        Displays the copyright message for the png or jpg
ct_boxplot.c             Main source code (Screen oriented)
ct_boxplot_read_ct.inc   Reads the ct files
ct_boxplot.doc           This file
ct_boxplot.h             General .h file
ct_boxplot_general.inc     General functions
ct_boxplot_ps.inc          Generates postscript output
ct_boxplot_img.inc         Generates png/jpg output
Makefile_ct              Makefile for ct_boxplot

This program reads multiple ct files and displays them. It can create
png,jpg or postscript output.

 'png' and 'jpg' are used interchangably throughout this document.

The png/jpg output is limited to the zoom window.

If the dots in the zoom window are large enough,
the program displays a dot in multiple colors to indicate which
structure produces overlap at this point.

If the dots are too small for this, the dot is displayed as gray
for partial overlap, or black for full overlap.

The lower triangle of the display always uses black or gray for
overlap.  Which structure, if any, for the lower display can be chosen
from the menu.

The png,jpg and ps output should match the screen.  When they switch
from multiple colors to black and gray for showing overlap depends 
on the dot size.  They do not switch at exactly they same time as
the screen.  It depends on how many pixels or points are available
for each color based on the dot size. Alter STRIPE_PS,STRIPE_GIF,
STRIPE_SCREEN in ct_boxplot.h to alter when this happens. 

There is a menu feature, partial overlap color, show gray as multicolor
in zoom that forces
multiple colors for the overlap.

ct_boxplot.col is read at execution time and can be edited for
user preference.

This file is searched for in 1. The present working directory,
                             2. The directory specified by environmental
                                variable "MFOLDLIB"
                             3. The directory dat with the directory
                                specified by the environmental variable
                                "MFOLD" 

______________________________________________________________________
Each ct file must contain only one structure.
It must start as: 
 
741 ENERGY =  -238.3    mok-lacZ + gtgtaa             
    1 G       0    2  618    1
    2 G       1    3  617    2
    3 C       2    4  616    3

The first line must contain the information shown.
The number of bases, energy and name are each taken from it.
The = is required too.

The number of bases is compared to the number in the file.
The first entry on each line after the first must indicate which base
is specified. The program will exit if there are any skips or duplicates.
They must start at 1.

The program warns against The second entry, the base, being different
within different CT files.

All ct files on a given run must be the same length.

________________________________________________________________________
Sample usage:

ct_boxplot name1.ct name2.ct name3.ct 


The program accepts 1 to 200 ct files.
Only one color is used for files 15 to 200.
The text window indicates which files
correspond to each dot when 80 or less
ct files are used.  Click on a dot with the right
mouse button to observe this.


Valid arguments:

-b            Enable clear png/jpg background
               (I am not sure this works.)

-d direct/   Look for ct files in directory direct

-o name_out  Specify name of output file as               
              name_out.ps, name_out.png, or name_out.jpg                  

-s           Save the tgd file for editing the png/jpg

-t "TITLE"   Use TITLE as a title rather than the first line of the
             first ct file. (Quotes are required.)




Within the main screen or zoom window.
1.  The left button is for clicking on dots for identification.
2.  The right button activates the menu.
3.  The middle button is pressed to select the top left corner of a 
    zoom window.  Releasing the button selects the bottom
    right corner.  





The program requires use of GLUT by Mark Kilgard for
use of OpenGL





The program requires the use of tgd by Bradly K. Sherman and gd 1.8.1
by Thomas Boutell for png/jpg creation.
The tgd has been altered by Darrin Stewart. 
It originally used gd 1.2




The postscript output is now easy to alter to adjust the colors,
or the size of dots.  In particular, it is possible to make
dots of a particular structure larger to emphasize it.  If enlarged,
it will show up under its partial overlap dots.

For many structures, it is possible to change the color for 
a particular structure to see it. While the program uses the
same for color for structure beyond 15, a particular color can
be set here. In fact, for 50 structures, all 50 can be set to different
colors.

The postscript and screen output contains counts for each type of dot.
For 3 sequences,
if they are interpreted for content, the count is for the upper triangle
when it is turned on there with -i or from the menu with partial overlap
color, show gray interpreted for content.
If it is displayed in the lower triangle only with -a -10 or structure for
lower triangle, partial overlap interpreted,
then the count applies there.

Most counts only count dots in the upper triangle.

Counts for individual sequences count the dots shown in that color as
well as those of the sequence used for partial or full overlap.



The big dot on/off causes dots on the screen to be shown with a minimum of
1 pixels or a minimum of 4 pixels.  The default is ON at 4 pixels.
For the postscript, the alt option creates postscript dots at least 1/72 inch
in size.  The normal way is to draw the dots as large as possible without
overlapping each other.  See the postscript file for fine adjustments
to dot sizes.



Summary of changes made of May 4,

1.  The alt option on ct_boxplot under create postscript output,
will now work and force all dots to be at least 1/72 inch in size.

2.  If you wish, the size of each type of dot can be altered from a
single
line within the postscript.  For structure i, alter si.  1 is normal
size.
A value to create dots 1/72 inch is given in the file.

The size of partial overlap dots can be altered, but for 3 sequences
when
the color depends on content,
all of the  dots are given the same size as specified by s1.

When a single partial overlap dot is shown in multiple colors,
zs2,zs3,zs4, etc describe the size of each of its
components.

Useful:
For partial overlap shown as gray, enlarging dots for a single sequence
will make its dot appear
under the gray dot and show where it occurs.


3.  I have added all sorts of counts for types of dots on screen and in
    the postscript output.


4.  For 3 sequences, partial overlap interpreted for content can be
    chosen in the upper or lower
    triangle.

5.  The menu option
        -d direct/
     will look for ct files in the directory:  direct or whatever name
     is selected.

6.  Colors for each type of dot can be easily specified.  Any structure
    can be colored uniquely,
    including those past 15 that are shown as a single color.  In fact, for
    50 structure,
    they can be displayed in 50 colors if desired.

7.  ct_boxplot_ng has the same features with new flags,
     -f  force gray as multicolor,
     -i  force gray interpreted for content in upper triangle  (only for
         3 structures).
     -a  -10    show gray interpreted for content in lower triangle
         (only for 3 structures).
     -j draw postscript dots at least 1/72 inch in size




    ________________
    |Special Keys: |  (Added December 14, 1999)
    |______________|


CURSOR-UP,DOWN,RIGHT,LEFT:  Move zoom window up,left,right,down from
                            main or zoom window.

PAGE-UP,PAGE-DOWN:          Zoom in or out from main or zoom window.