Documentation for overlay_boxplot

Feb 4, 1999

by Darrin Stewart and Michael Zuker

Documentation for overlay_boxplot

*****************************************************************************
Files **
********

overlay_boxplot_setcolor.inc  Sets the colors
overlay_boxplot.col           List of colors to use 
copyright_ps.inc              Displays the copyright message  the ps output
copyright_gif.inc             Displays the copyright message for the GIF
overlay_boxplot.c             Main source code (Screen oriented)
overlay_boxplot_read_ct.inc   Reads the ct files
overlay_boxplot.doc           This file
overlay_boxplot.inc           General .inc file
overlay_boxplot_ps.inc        Generates postscript output
overlay_boxplot_gif.inc       Generates GIF output
Makefile_overlay              Makefile for overlay_boxplot


Output: name.ovr-opt.ps or name.ovr-ct.ps for optimal mode or ct mode when
        name.plot is the input file.

        name.ovr-opt.gif or name.ovr-ct.gif for optimal mode or ct mode when
        name.plot is the input file.

***************************************************************************
Description **
**************


This program reads a ct file and displays it over a plot file.
When a dot from a ct file is on top of an optimal dot from the plot file,
it is shown as green.  It is red for a nonoptimal, and yellow for a close
to optimal.  Red is also used when the dot from the ct file misses
a plot file dot completely.  The increment option applies only to
the plot file.  The filter applies only to the non-optimal dots
of the plot file.



______________________________________________________________________

In Optimal Mode:

This program reads a ct file and displays it over a plot file.
When a dot from a ct file is on top of an optimal dot from the plot file,
it is shown as green. Plot file dots that miss CT dots are red. Plot file dots
within the specified distance of a ct dot are yellow.  Ct dots that miss optimal dots are cyan. The increment option applies only to
the plot file.  The filter applies only to the non-optimal dots
of the plot file.

_________________________________________________________________________
The program can create gif or postscript output.

The GIF output is limited to the zoom window.

************************************************************************
Requirements **
***************


overlay_boxplot.col is read at execution time and can be edited for
user preference.  It allows for some adjustment of the dot sizes, but it
is probably hard to make better.  The program contains some code to 
improve appearance independent of these values.

overlay_boxplot.col is searched for in
                             1. The present working directory,
                             2. The directory specified by environmental
                                variable "MFOLDLIB"
                             3. The directory dat with the directory
                                specified by the environmental variable
                                "MFOLD" 

______________________________________________________________________
The ct file must contain only one structure.
It must start as: 
 
741 ENERGY =  -238.3    mok-lacZ + gtgtaa             
    1 G       0    2  618    1
    2 G       1    3  617    2
    3 C       2    4  616    3

The first line must contain the information shown.
The number of bases, energy and name are each taken from it.
The = is required too.
(The above is expected, but only the number of bases is required)

The number of bases is compared to the number in the file.
The first entry on each line after the first must indicate which base
is specified. The program will exit if there are any skips or duplicates.
They must start at 1.


**************************************************************************
Sample usage: **
****************

overlay_boxplot name1.ct name2.plot 


The .ct and .plot are optional.  The program does not
care which is first, but for:
ct_boxplot name1 name
name1 is tried as a plot, then as a ct, name2 is tried as the other.



Valid arguments:

-b            Enable clear GIF background

-o name_out  Specify name of output file as               
              name_out.ps or name_out.gif                  

-s           Save the tgd file for editing the gif

-t "TITLE"   Use TITLE as a title rather than the first line of the
             first ct file. (Quotes are required.)




Within the main screen or zoom window.
1.  The left button is for clicking on dots for identification.
2.  The right button activates the menu.
3.  The middle button is pressed to select the top left corner of a 
    zoom window.  Releasing the button selects the bottom
    right corner.  

For the counting of base pairs, (CT Mode)
  Dots in the lower right triangle are never counted.
  The counts apply to dots shown in the zoom window or full window
   depending on which is shown as output.
  The number in the text color is the number of plot file dots.
  The green is for the green or optimal ct dots.
  The yellow is for the close to optimal yellow dots.
  The red is for the Not close to optimal red dots.
  The overlap yellow is for yellow dots that have plot dots on top
  of them.
  The red overlap is for red dots that have gray dots on top of them.
  The black beside the green is the number of optimal plot dots.
  By selecting a proper filter, it is possible to have yellow dots
  without gray dots on top of them.
  
If the dots are too small, the gray dots may not be drawn on top of the 
  yellow, or red dots, but the counting is performed is if the dots were drawn.

For the counting of base pairs, (Optimal Mode)
 Similar to above, except cyan are ct dots that miss, green are
  optimal that overlap ct dots, yellow are optimal dots within a distance
  of the ct dots. The cyan dots are drawn on top of gray dots, but
  no overlap counting is done.



The filter and increment do not affect the drawing of red, or yellow dots.


The filter does not affect the drawing of green or optimal plot dots.

The program requires use of GLUT by Mark Kilgard for
use of OpenGL



The program requires the use of tgd by Bradly K. Sherman and g.d 1.1.1
by Thomas Boutell for GIF creation.



*****************************************************************************
Summary: **
*****************




Default is to color the CT file dots based on how they overlap   
 the optimal dots.                                                
         Green for overlap,                                       
         Yellow within the energy specified with close            
         and red for all others.                                  
 With the Optimal mode,  Optimal dots are colored.                
          Green for overlap with ct dots,                         
          Yellow for within the close distance specified          
          and red otherwise.                                      
          Unused ct dots are cyan                                 

For the ct mode, the default close energy is 10% of the range in the
plot file.

The default close distance is 0 for optimal mode.





    ________________
    |Special Keys: |  (Added December 14, 1999)
    |______________|


CURSOR-UP,DOWN,RIGHT,LEFT:  Move zoom window up,left,right,down from
                            main or zoom window.

PAGE-UP,PAGE-DOWN:          Zoom in or out from main or zoom window.